## Slide 1: The FROG Multi-Domain Orchestrator
Ivano Cerrato, Fulvio Risso
Politecnico di Torino

## Slide 2: Outline
FROG architecture, data formalism and operations
Use case example: deploying per user services
Deploying FROG on JOLNET

## Slide 3: FROG Architecture and Operations
Ivano Cerrato, Fulvio Risso
Politecnico di Torino

## Slide 4: Introduction
The infrastructure of a telco operator includes several (and very different) technological domains, each one with strengths and weaknesses
  SDN network, POP/cloud datacenters, CPEs, IoT @ edge
Objective: define an orchestration system that can deploy generic services while possibly exploiting all the available resources and capabilities present in the infrastructure
  1) End-to-end service orchestration and deployment
  2) Arbitrary orchestration of generic services
  3) Support for arbitrary resources and capabilities
  4) Possibly, use unmodified technology-specific orchestrators
SDN network
Mobile Access
Data center
SDN controller
Residential gateway
Technological domain
OpenStack controller
5G access infrastructure
Internet
CPE controller

## Slide 5
NFV orchestrator
SDN Domain Orchestrator
Message bus: transports YANG data models using pub/sub model
OpenStack Domain Orchestrator
Per-user services orchestrator
Telco cloud datacenter
Telco SDN network
Universal Node Domain Orchestrator
Resource-constrained CPE
NFV configurations orchestrator
Residential Gateway Data Model
list ethernet {
leaf name { type string; }
leaf address { type ip4addr; }
leaf netmask { type ip4mask; }
}
list wifi {
leaf SSID { type string; }
leaf address { type ip4addr; }
leaf netmask { type ip4mask; }
}
VM Firewall
SDN Domain Data Model
object sw-bundles {
capability BridgedLAN;
capability TrafficSteering;
capability GenericBundle;
}
object BridgedLAN {
leaf NetworkAddr {type ip4addr; }
leaf DefGwAddr {type ip4addr; }
leaf DHCP {type boolean; }
...
}
Firewall Data Model
list policyEntry {
leaf policy-id { type uint16; }
leaf action {
type enumeration {
enum DROP;
enum ALLOW;
}
}
leaf interface {
type leafref {
path "/fw/ifName";
}
}
leaf saddress { type ip4addr; }
leaf daddress { type ip4addr; }
leaf sport { type portnumber; }
leaf dport { type portnumber; }
}
Webcam Data Model
object webcam {
leaf dpiresolution { type uint16; }
leaf location { type string; }
leaf outdoor { type boolean; }
}
Infrastructure configurations orchestrator
Personal video surveillance service orchestrator
FROG overview

## Slide 6: FROG principles
Each object (e.g., technological domain) is associated with a description written according to a unified (between all the objects) YANG data-model
  The description is published on the message bus, which can deliver it to all the interested modules (e.g., the ones that subscribed for it, such as the FROG orchestrator)
The message bus interconnects all the services (a.k.a., orchestrators, object)
  Domain orchestrators, FROG orchestrator and other applications that, e.g., take care of the service logic
  Operates according to the pub/sub paradigm
    Each message/information is associated with a specific topic
    Modules interested in some information subscribe to the proper topic
Domain orchestrator operate on top of each technological domain
  The domain orchestrator knows the internal details of the underlying domain
  Allows the integration of vanilla controllers, hence domains, in the FROG framework

## Slide 7: NFV orchestration architecture (1)
CPE controller
SDN network
Data center
SDN controller
FROG orchestrator
Domain orchestrator
Domain orchestrator
Adv. blocker
Private cache
Residential gateway
Domain orchestrator
Firewall
Private cache
Adv.
blocker
Firewall
Technological domain
OpenStack controller
Internet
Service graph (REST)
Domain description
(message bus)
FROG WEB GUI
Service layer
(e.g., per-user service graphs)
Firewall

## Slide 8: NFV orchestration architecture (2)
Multi-domain orchestration architecture
  Capable to deploy service graphs on heterogeneous technological domains
    E.g., SDN network, data center, CPE
Two orchestration layers
  FROG orchestrator
    Overarching (or multi-domain) orchestrator
    Selects the most suitable domain(s) involved in the service deployment
      Based on the description of each domain provided by the domain orchestrator
    Instructs each domain orchestrator to deploy (a portion of) the original service graph
    Through its northbound API receives requests of service graphs to be deployed (e.g., from a service layer application)
    Through its southbound API interacts with the domain orchestrators
      Receives the description of each domain (through message bus)
      Provides to the proper domain orchestrator the (part of) service graph to be deployed in a domain (through REST interface)
  Domain orchestrators [...]

## Slide 9: NFV orchestration architecture (3)
Two orchestration layers
  FROG orchestrator [...]
  Domain orchestrator
    One per domain
    Knows all the internal details of the underlying domain
    Through its northbound API
      Exports the domain description (through message bus)
      Receives service graphs to be deployed on the domain under its control (through REST interface)
    Through its southbound API, interacts with the vanilla infrastructure-specific domain controller to fulfill requests coming from the FROG orchestrator
      ONOS/OpenDaylight in case of SDN domain
      Nova, Neutron (and the SDN controller) in case of OpenStack-based domain
      And more

## Slide 10: Data flows and APIs (1)
Two flows of information
  North-south:
    From service layer to FROG orchestrator
    From FROG orchestrator to domain orchestrators
    Carries service graphs described according to the NF-FG formalism
    Based on a REST interface
    CRUD (create, read, update, delete) operations supported on service graphs
  South-north
    […]

## Slide 11: Data flows and APIs (2)
Two flows of information
  […]
  South-north
    Carries the domains description from domain orchestrators to the other modules that are part of the FROG framework
    Based on a message bus that allows communication through the publisher/subscriber paradigm
      The interested modules (e.g., the FROG orchestrator) subscribe to a specific topic
      The domain orchestrators publish the domains description on that specific topic
    A broker module is actually in between all the modules that are part of FROG
    The message bus allows the FROG architecture to be easily extended with new modules that are interested in information about domains
      E.g., new service layer applications

## Slide 12: Domain description (1)
To enable the FROG orchestrator to deal with heterogeneous domains, FROG defines a common data model for domains
  Based on YANG
  Describes the domain both from the point of view of the computing and from the point of view of the networking
The FROG orchestrator does not know anything about a domain but the information in the domain description
Domain Data Model
leaf id { ... }
list interface {
container connection-capabilities {
list neighbor {
leaf id { ... }
leaf type {
enumeration {
domain; legacy-net; access-net;
}
}
list labeling-methods {
leaf name {
enumeration { VLAN, GRE, … }
}
list available-labels { ... }
leaf preference{ type uint8 { range “0 .. 10” } }
}
uses openconfig-interface;
}
list functional-capabilities {
type identityref { base “functional-capability”; }
}

## Slide 13: Domain description (2)
Firewall
NAT
VPN
if-3
If-2
. . .
neighbor:
id: internet
type: legacy-net
. . .
Internet
domain-A
Image repository
NAT A
Tech: KVM [. . .]
VPN A
Tech: Docker [. . .]
domain-A abstraction
domain-A Orchestrator
if-3
if-2
if-1
Firewall Data Model
leaf ports# {
type uint8;
value max;
}
leaf iso/osi level {
type uint8 { range “1 .. 7” }
...
}
leaf dmz {
type Boolean;
...
}
Domain Data Model
leaf id { ... }
list interface {
container connection-capabilities {
list neighbor {
leaf id { ... }
leaf type {
enumeration {
domain; legacy-net; access-net;
}
}
list labeling-method {
leaf name {
enumeration { VLAN, GRE, … }
}
list available-labels { ... }
leaf preference{ type uint8 { range “0 .. 10” } }
}
uses openconfig-interface;
}
list functional-capabilities {
type identityref { base “functional-capability”; }
}
NAT Data Model
[...]
VPN Data Model
[...]
Firewall
ports#: 3
iso/osi level: 4
dmz: true
If-1
speed: 10 Gbps
IPv4-address: 10.0.0.1
connection-capabilities:
neighbor:
id: domain-B
type: domain
labeling-methods:
VLAN
- available-labels: { 25, 26 }
- preference: 4
GRE
- available-labels: {…}
- preference: 10
VXLAN { . . . }
. . .
Functional capabilities
OpenStack Controller
domain-B Orchestrator
domain-B
domain-B abstraction
NAT Data Model
[...]
SDN Controller
Firewall A
Tech: Docker
RAM: 290 MB
Firewall B
Tech: KVM
RAM: 1240 MB

## Slide 14: Computing information
From the point of view of computing, a domain is associated with what we called “functional capabilities”
A functional capability represents the ability of the domain to execute a given NF
No matter how it is actually implemented
  The NF description is just from a functional point of view
    E.g., hardware firewall and VM firewall could be modeled by the same functional capability
  Does not include any information about the resources needed for its execution
    E.g., amount of CPU and RAM
  Some examples:
    A VM image in a data center
    A software bundle in an SDN controller
    An hardware module in a CPE
Hardware
Firewall
Virtual
Machine
Firewall
Functional
Capability
Available
Function
Firewall
Ports: 2
Throughput: 10 Gbps
Firewall
Ports: 2
Throughput: 10 Gbps

## Slide 15: Networking information (1)
From the point of view of networking, a domain is described as a big switch with a number of interfaces
Interfaces of the big-switch represent a connection point to the rest of the world
Each interface is associated with a set of “connection capabilities”
  Neighbor indicates what can be directly reached through that interface
    Another domain
    An access network connected to end users
    A legacy network: network delivering packets
    according to, e.g., traditional routing
if-1
if-2
if-3
if-4
Domain Infrastructure
domain-B
Internet
domain-C
Access Network

## Slide 16: Networking information (2)
Each interface is associated with a set of Connection Capabilities
  Neighbor [...]
  Labeling methods
    Indicates the ability of the domain to:
      Classify incoming traffic based on specific patterns (e.g., VLAN ID, GRE tunnel key)
      Modify outgoing traffic so that it satisfies a specific pattern (e.g., encapsulating into a specific GRE tunnel)
    Inter-domain traffic steering technology is associated with the list of “labels” still available
      E.g., VLAN ID, GRE key
  Other interface parameters (e.g., IP configuration)
if-1
if-2
if-3
if-4
Domain Infrastructure
domain-B
Internet
domain-C
Access Network

## Slide 17: FROG orchestrator – The virtual topology (1)
Thanks to the domain descriptions exported by domain orchestrators, the FROG orchestrator sees the network infrastructure as a set of domains
  Associated with a set of functional capabilities
  Interconnected through “virtual channels”
  The FROG orchestrator is not aware of the nature of the domain (e.g., it does not know whether the selected domain is an SDN network or a data center)
domain-A
domain-B
IPv4: 10.0.0.1
VLAN (25,28): preference 5
GRE (0x03,0x04): preference 4
IPv4: 10.0.0.2
VLAN (25,28): preference 5
GRE (0x03,0x04): preference 4
VLAN 25, 28
GRE 0x03, 0x04
Internet
legacy network
if-1
if-0
if-1
Access network
if-0
domain-C
backbone
legacy network
if-2
if-0

## Slide 18: FROG orchestrator – The virtual topology (2)
The virtual topology is created using the following information
  The “neighbor” parameter indicates whether a connection between two interfaces (of different domains) may exist or not
  a virtual channel is actually established between two interfaces per each pair <labeling-method, available-label> they have in common
    Virtual channels can be established also through domains attached to a legacy network

## Slide 19: Network Functions – Forwarding Graph (1)
Formalism that describes a service graph
  Based on JSON
  Describes VNFs, endpoints and flow-rules (i.e., links)
Network Functions – Forwarding Graph
NAT
L2 switch
DHCP server
L2Port:0
L2Port:1
L2Port:2
Inout:0
WAN:0
USER:0
Firewall
Inout:0
Inout:1
endpoint-1
domain: domain-A
interface: if-0
Input-traffic:
- eth-src: aa:bb:cc:dd:ee:ff
endpoint-2
domain: domain-B
interface: gre0
- from: 130.192.225.125
- to: 5.87.194.144
- key: 0x26

## Slide 20: Network Functions – Forwarding Graph (2)
{
"forwarding-graph":
{
"id": "0x1",
"name": "Forwarding graph",
"VNFs": [
{
"id": "0x1",
"name": "firewall",
"ports": [
{
"id": “p0",
"name": "data-port"
},
...
]
}
],
"end-points": [
{
"id": "0x1",
"name": "ingress",
"type": "interface",
"interface": {
"if-name": "eth1"
}
},
...
],
"big-switch":
{
"flow-rules": [
{
"id": "0x1",
"priority": 10,
"match": {
"port_in": "endpoint:0x1"
},
"actions": [
{
"output_to_port": "vnf:0x1:p0"
}
],
},
…
]
}
}
}
Firewall

## Slide 21: Network Functions – Forwarding Graph (3)
Describes the service graph through three main sections
  VNFs: indicates the VNFs to be deployed
    A VNF can be associated with a specific template, which describes the specific VNF implementation to be deployed
    In case the VNF is not associated with any template, the specific implementation will be then selected by the domain orchestrator in charge of deploying it
  end-points: represent the entry/exit points of the traffic in/from the service graph
    May be characterized with the traffic that has to enter/exit in/from the service graph through that endpoint
      Traffic specifiers
        E.g., IP addresses, VLANs
      Physical specifiers
        E.g., the entry point of such a traffic in the operator network
  big-switch: includes the rules that describe the links between the VNF ports and the endpoints
    Rules are specified through an OpenFlow-like syntax
      Priority
      Match
      Action

## Slide 22: FROG orchestration
Service graph
FROG orchestrator
sap-0
web traffic
other traffic
other traffic
web traffic
Firewall
Web cache
NAT
sap-1
domain: domain-A
interface: if-0
Input-traffic:
eth-src: aa:bb:cc:dd:ee:ff
domain: domain-C
interface: if-1
IPv4: 10.0.0.1
VLAN (25,28), GRE (0x03,0x04)
VLAN 25,
28
IPv4: 10.0.1.1
GRE (0x01,0xA3)
GRE 0x01,
0x03
if-1
Virtual topology
Internet
if-1
if-0
IPv4: 10.0.1.2
GRE (0x01,0xA3)
if-1
if-0
Access network
if-0
IPv4: 10.0.0.2
VLAN (25,28), GRE (0x03,0x04)
sap-0
web traffic
other traffic
Firewall
sap-2
sap-3
sap-4
Sap-6
sap-5
sap-7
web traffic
Web cache
NAT
sap-1
sap-8
sap-9
interface: if-1
labeling-method: VLAN
vlan-id: 25
interface: if-0
labeling-method: VLAN
vlan-id: 25
interface: if-1
labeling-method: GRE
local: IP 10.0.1.1
remote IP: 10.0.1.2
key: 0x03
interface: if-0
labeling-method: GRE
local IP: 10.0.1.2
remote IP: 10.0.1.1
key: 0x03
interface: if-1
interface: if-0
interface: if-1
labeling-method: VLAN
vlan-id: 28
interface: if-0
labeling-method: VLAN
vlan-id: 28
other traffic
VLAN 28
VLAN 25
GRE 0x01
GRE 0x03
if-1
if-0
if-1
if-0
if-1
if-0
if-1
if-0
if-1
if-1
interface: if-1
labeling-method: GRE
local IP: 10.0.1.1
remote IP: 10.0.1.2
key: 0x01
interface: if-0
labeling-method: GRE
local IP: 10.0.1.2
remote IP: 10.0.1.1
key: 0x01

## Slide 23: FROG orchestration operations (1)
When receives a service graph to be deployed, the FROG orchestrator executes the following steps:
  Identify best domain(s) that will actually implement the required NFs, links and endpoints
    The FROG orchestrator uses a greedy approach that minimizes the distance between two VNFs/endpoints directly connected in the service graph
      Other algorithms may be defined/exploited
  Constraints:
    Some endpoints are forced to be mapped to specific domain interfaces
      E.g., because they represent the entry point of the user traffic into the network
    A VNF must be executed in a domain that advertises the corresponding functional capability
    Links between VNFs/endpoints deployed in different domains require the exploitation of virtual channels for inter-domain traffic steering

## Slide 24: FROG orchestration operations (2)
The output of the placement algorithm is one sub-graph per each domain involved
  This sub-graph includes
    VNFs assigned to that domain
    Possibly, new endpoints generated during the placement process
      Originated by links that connects VNFs/endpoints mapped to different domains
      Two endpoints originated by the same link are connected through a virtual channel
If VNFs are assigned to two domains connected by means of a third domain
  An additional sub-graph is generated for the intermediate domain as well
  This sub-graph just includes network connections and endpoints

## Slide 25: Inter-domain traffic steering (1)
sap-2
sap-3
interface: if-1
technology: VLAN
vlan-id: 28
interface: if-0
technology: VLAN
vlan-id: 28
interface: if-1
technology: VLAN
vlan-id: 25
interface: if-0
technology: VLAN
vlan-id: 25
if-1
if-0
pkt
pkt
vlan 28
sap-4
sap-5
pkt
pkt
physical connection
domain-A
domain-B
pkt
vlan 25
pkt

## Slide 26: Inter-domain traffic steering (2)
Each endpoint is characterized by information of the virtual channel connected to it
  This enables each domain orchestrators to properly set up the inter-domain traffic steering
    Packets sent through a specific endpoint must be properly labeled (e.g., tagged) before being sent through the associated interface
    Packets received from an interface with a particular label must be forwarded to a specific endpoint
  The label should only be used to implement the inter-domain traffic steering
    Packets should be tagged/encapsulated just before being sent out of the domain
    The tag/encapsulation should be removed just after the packet classification in the next domain

## Slide 27: Domain orchestrators (1)
Allow the integration of vanilla domains in the FROG orchestration framework
Through the interaction with the vanilla domain controller, the domain orchestrator retrieves domain information
    This is then exported on the message bus according to the domain data-model
      At the boot and each time something changes in the domain
Convert the service graph in calls to the northbound API exposed by the vanilla domain controller
    Start the required VNFs
    Configure the links among them
    Set up the inter-domain traffic steering (thanks to the information associated with the endpoints)
[…]

## Slide 28: Domain orchestrators (2)
[…]
We have defined three domain orchestrators, capable to deploy service graphs in different domains
  OpenStack-based data center
    OpenStack to manage virtual machines and intra-domain traffic steering
    (optional) ONOS/OpenDaylight to manage the inter-domain traffic steering
  SDN network under the control of ONOS or OpenDaylight
  Universal node
    Lightweight orchestrator for resource-constrained devices (e.g., CPE)
    Can start VNFs in virtual machines, Docker containers and on the bare metal

## Slide 29: The SDN domain
The SDN domain consists of
  A set of OpenFlow switches
  An SDN controller (we support ONOS and OpenDaylight)
The SDN domain orchestrator interacts with the vanilla controller in order to
  Retrieve domain information to be exposed on the message bus
    E.g., boundary interfaces and available VNFs
      VNFs are implemented as software bundles executed in the SDN controller
  Create network paths and start the software bundles implementing the required VNFs
    Use VLAN tags to set up intra-domain paths
Limitations
  Service graphs must not include two chained VNFs
  ONOS and OpenDaylight do not support multiple instances of the same software bundle
    If needed, multi-tenancy must be managed by the software bundle code

## Slide 30: The OpenStack-based domain (1)
OpenStack
Controller
Nova server
Compute node(s)
OvS daemon
br-int
br-ext
Hypervisor
Service graph
OpenStack domain orchestrator
Domain information
Nova agent
Network node
Neutron agent
SDN controller (ONOS/ODL)
Datacenter physical network
VM
OvS daemon
br-ext
OpenStack
images repository
Neutron server
Neutron agent
Datacenter exit interface
Private cache
Firewall

## Slide 31: The OpenStack-based domain (2)
To deploy a service graph, the domain orchestrator executes the following steps:
  Interacts with Neutron to create
    One internal network for each link of the service graph
  Interacts with Nova in order to start the VNFs (as virtual machines)
    Virtual machines images are store in the OpenStack image repository (i.e., Glance)
    Nova, in turn, interacts with Neutron to create VNF ports and connect them to the proper internal network
  Interacts with the SDN controller to create links towards the external world and set up the inter-domain traffic steering
    OpenStack is in fact not able to manage such connections, but only connections among virtual machines (i.e., intra-domain)
    Through the SDN controller, the domain orchestrator
      Creates the proper links towards the external world
      Configures the network so that traffic that exits/enters the datacenter is properly encapsulated/decapsulated, according to the information associated with the graph endpoints

## Slide 32: Getting started with FROG
FROG orchestrator
SDN Domain Orchestrator
OpenStack Domain Orchestrator
Telco cloud datacenter
Telco SDN network
Universal Node Domain Orchestrator
Resource-constrained CPE
https://github.com/netgroup-polito/frog4
FROG WEB GUI
Per-user services orchestrator
Message bus

## Slide 33: Dynamic deployment of per-user service graphs
Ivano Cerrato, Fulvio Risso
Politecnico di Torino

## Slide 34: Use case description
Goal: instantiate per-user services when the user connect to the network
  We have to provide the same service regardless of the device used by the end user, and regardless of his connection point to the network
  Traffic belonging to different end users must be processed by different service graphs
    Each end user may in fact require a different service from the network
This requires to intercept all traffic entering into the network
  Traffic of authenticated users must then be processed in the proper per-user service graph
  Unauthenticated users must be authenticated, so that their own service graph can be instantiated

## Slide 35: Authentication graph (1)
To authenticate new users, we defined the “authentication service graph”
  Attached to all the domain interfaces connected to access networks
  Processes all the traffic coming from those interfaces and belonging to unauthenticated users
  Deployed by service layer orchestrator at the bootstrap
    The service layer orchestrator retrieves information about access ports though the message bus
      Particularly, this information is included in the domains descriptions
    Then it dynamically updates the authentication graph so that it is attached to all the access ports
This graph performs the following operations
  User authentication
  Retrieve the current location of the user (e.g., the domain/interface to which he is connected)
  Retrieve the identifier of the device (i.e., MAC address) he is currently using
This information is then provided to the service layer orchestrator

## Slide 36: Authentication graph (2)
Web captive portal
OpenFlow controller
L2 + OpenfFow switch
ISP graph
Authentication graph
CPE-1
– wlan0
CPE-2
– wlan0
CPE-2
– eth0
CPE-2
– eth1
CPE-1
(Universal Node)
Telco network
(ISP)
DataCenter
(OpenStack)
CPE-2
(Universal Node)
Reference scenario

## Slide 37: Authentication graph (3)
Web captive portal
OpenFlow controller
L2 + OpenfFow switch
ISP graph
Data center
gre0
gre1
gre2
gre3
wan0
gre0
CPE-1
wan0
gre1
CPE-2
eth0
gre2
eth1
gre3
CPE-1
(Universal Node)
Telco network
(ISP)
DataCenter
(OpenStack)
CPE-2
(Universal Node)
Reference scenario

## Slide 38: ISP graph
Provides basic network services to the other service graphs
  This way, we don’t have to replicate those VNFs in all the user graphs
It is entirely deployed in the data center
DHCP server
Router + NAT
L2 switch
Data center
– eth1
Auth graph
Usr graph 1
…
Usr graph N
ISP graph

## Slide 39: User graph – Green user connected to CPE-1
Firewall
ISP graph
CPE-1 – wlan0
Src mac: user green device
Green user graph
wan0
gre4
Data center
Src mac: user green device
Firewall
ISP graph
CPE-1
Information dynamically added by the service layer
Retrieved through the authentication graph
gre4
CPE-1
(Universal Node)
Telco network
(ISP)
DataCenter
(OpenStack)
CPE-2
(Universal Node)
Reference scenario

## Slide 40: User graph – Blue user connected to CPE-2
wan0
gre5
CPE-2
Src mac: user green device
Firewall
ISP graph
Data center
gre5
Firewall
ISP graph
CPE-1 – wlan0
Src mac: user green device
Green user graph
Information dynamically added by the service layer
Retrieved through the authentication graph
CPE-1
(Universal Node)
Telco network
(ISP)
DataCenter
(OpenStack)
CPE-2
(Universal Node)
Reference scenario

## Slide 41: Deploying FROG on JOLnet
Ivano Cerrato, Fulvio Risso
Politecnico di Torino

## Slide 42: The JOLnet (1)
Network
  Each tenant is associated with a slice
  Each slice is associate to a set of VLANs
    E.g., POLITO has VLANs: 280-289
  Each slice is controlled by a given SDN Controller
    In the POLITO slice, all the switches are configured to interact with the ONOS controller available at “130.192.225.92”
Controllers (TILAB, Torino)
Core
(TO-Poli)
CPE
(TO-Poli)
Core
(Pisa)
CPE
(Pisa)
Core
(Tilab)
CPE
(Tilab)
CPE
(Milano)
Core
(Milano)

## Slide 43: The JOLnet (2)
Computing
  OpenStack Icehouse is used
  External networks
    Cannot be created by tenants
    Already created by the admin, each one associated with a given VLAN
      E.g., POLITO has VLANs: 280-289
    The traffic of an external network enters/exits the SDN network with the proper VLAN tag
      VMs receive/generate untagged traffic
  Tenants can:
    Create VMs, create internal networks (i.e., between VMs), and attach VMs to internal and external networks
Controllers (TILAB, Torino)
Core
(TO-Poli)
CPE
(TO-Poli)
Core
(Pisa)
CPE
(Pisa)
Core
(Tilab)
CPE
(Tilab)
CPE
(Milano)
Core
(Milano)

## Slide 44: Adapting FROG for JOLNET
Domain orchestrators have been slightly modified to be deployed on JOLnet
  SDN domain
    Inter-domain traffic steering (between the OpenStack and the SDN domains) is done exclusively using VLAN tags
      Only the tags identifying our slice in JOLNET can be used
    The SDN domain orchestrator implements paths in the SDN domain using VLAN tags as well
      Since JOLNET does not support QinQ, only the tags identifying our slice in JOLNET can then be used
  OpenStack domain
    The OpenStack domain orchestrator exploits existing external networks in order to realize the inter-domain traffic steering

## Slide 45: Starting the SDN domain orchestrator on JOLNET
…
[vlan]
#the following VLAN IDs correspond to our slice on JOLnet
#they are used for inter-domain and intra-domain traffic steering
available_ids = 270-279
…
[other_options]
…
# disable features that are not compatible with JOLnet Flowvisor
# * use VLANs for intra-domain traffic steering
# * use only the specified VLANs
jolnet = true
sdn-do.ini

## Slide 46: Starting the OpenStack domain orchestrator on JOLNET
[openstack_orchestrator]
…
# Specify where VNFs must be instantiated
availability_zone = AZ_TN
# Set the API version that the domain orchestrator must use to contact OpenStack
# This value can be 2 or 3 – Use 2 in JOLnet
identity_api_version = 2
…
[jolnet]
# Do not use the SDN orchestrator to set up inter-domain traffic steering,
# but a set of pre-created network
jolnet_mode = true
[networks]
# List of external networks that have to be used for inter-domain traffic steering
# e.g., exp270 is a network that will be associated with VLAN 270 in JOLnet
jolnet_networks = tn-mgmt, exp280, exp281, exp282, exp283, exp284, exp285, exp286, exp287, exp288
os-do.ini

## Slide 47: The POLITO slice on JOLnet
Access network (emulated using the OS AZ-TO)
SDN domain
TO
VLAN 270
TN
10.0.0.1
Mapped on VLAN 281
Port xyz
Port 123
R
Mapped on VLAN 280
OpenStack Domain

## Slide 48: SDN domain description
{
"frog-domain:informations": {
...
"frog-network-manager:informations": {
"openconfig-interfaces:interfaces": {
"openconfig-interfaces:interface": [
{
"name": "of:0x2/5108",
...
"openconfig-if-ethernet:ethernet": {
"openconfig-vlan:vlan": {
"openconfig-vlan:config": {
"interface-mode": "TRUNK",
"trunk-vlans": [
"278..289"
]
}
},
"frog-neighbor:neighbor": [
{
"remote-interface": "az_tn",
"domain-name": "openstack"
}
]
}
},
{
"name": "of:0x1/5104",
...
"openconfig-if-ethernet:ethernet": {
"openconfig-vlan:vlan": {
"openconfig-vlan:config": {
"interface-mode": "TRUNK",
"trunk-vlans": [
"280..289"
]
}
},
"frog-neighbor:neighbor": [
{
"remote-interface": "az_tn",
"domain-name": "openstack"
}
]
}
}
]
}
},
"type": "ONOS",
"capabilities": {
"infrastructural-capabilities": {
"infrastructural-capability": [...]
},
"functional-capabilities": {
"functional-capability": []
}
}
}
}

## Slide 49: OpenStack domain description
{
"frog-domain:informations": {
...
"management-address": "127.0.0.1:9200",
"frog-network-manager:informations": {
"openconfig-interfaces:interfaces": {
"openconfig-interfaces:interface": [
{
"state": {...},
"name": "az_tn",
"openconfig-if-ethernet:ethernet": {
"openconfig-vlan:vlan": {
"openconfig-vlan:config": {
"trunk-vlans": [
"270..279"
],
"interface-mode": "TRUNK"
}
},
"frog-neighbor:neighbor": [
{
"remote-interface": "of:0x2/5102",
"domain-name": "onos_domain"
}
]
},
"config": {
"enabled": true,
"description": "OS - AZ_TN",
"type": "ethernetCsmacd"
}
}
]
}
}
}
}